## Slide 1
Plant Whisperer
A plant that senses, predicts and talks back
IoT • Deep Neural Network • Generative AI

## Slide 2
Why plants need a voice
The problem
Plants are over- or under-watered because the signs show up late
Raw sensor numbers mean little to most people
Fixed thresholds ignore heat, light and humidity
Our idea
IoT sensors measure the environment continuously
A DNN predicts the hours until the soil is dry
An LLM turns it into a clear, friendly message

## Slide 3
System architecture
Sensors
Soil, DHT11 and LDR
ESP32
Reads and sends JSON over WiFi
DNN server
Flask + Keras predicts hours to dry
GenAI
Claude writes the plant's voice
Telegram
Message on mood change
IoT layer
DNN layer
GenAI layer
The DNN decides what is happening. The GenAI explains it.

## Slide 4
Hardware design and wiring
Soil moisture
GPIO34
DHT11
GPIO4
LDR + 10k
GPIO35
ESP32
3.3V logic
Bill of materials
ESP32 board ₹450
Soil sensor ₹80
DHT11 ₹120
LDR + resistor ₹30
Breadboard + wires ₹150
Total about ₹830
Prices are rough estimates and vary by seller. No soldering or custom PCB needed.

## Slide 5
Project budget
Chart: Hardware cost by item (INR, approx.)
| ESP32 board | Breadboard + wires | DHT11 | Soil sensor | LDR + resistor
Cost (INR) | 450 | 150 | 120 | 80 | 30
Software and services
Item | Cost
Arduino IDE | Free
Google Colab (training) | Free tier
Flask, Keras, Python | Open source
Telegram Bot API | Free
Claude API (LLM) | Usage-based, small
Total: about ₹830 in hardware. Software is free apart from small pay-per-use LLM charges.

## Slide 6
The DNN: predicting time to dry
Soil %
Temp
Humidity
Light %
Drying rate
Input (5)
Dense 32
Dense 16
Hours to dry
Chart: Hours to dry vs temperature
| 15°C | 20°C | 25°C | 30°C | 35°C | 40°C
Hours to dry | 38.9 | 28 | 21.9 | 17.9 | 15.2 | 13.2
From the synthetic drying model: soil 60%, light 50%, humidity 50%

## Slide 7
The GenAI layer: giving the plant a voice
Thirsty
soil below 25%
Happy
soil 25% to 80%
Drowning
soil above 80%
Telegram message (illustrative)
Soil is at 22%. The DNN says I will be crispy in about 3 hours. Water me, human.
Just watered you. How do you feel?
Finally. I forgive you.

## Slide 8
Project status
Completed
ESP32 firmware written
DNN trained, validation error about 0.7 h on synthetic data
Server, Claude and Telegram pipeline working
Hardware simulator drives the live demo
In progress
Assemble sensors and wiring
Calibrate soil and light readings
Fine-tune the DNN on real logged data

## Slide 9
Conclusion and future scope
What we built
End-to-end IoT, DNN and GenAI pipeline
Software pipeline complete; hardware build is about ₹830
Each layer has a distinct, real job
Next steps
Fine-tune the DNN on real logged data
Try an LSTM on time-series readings
Add a pump for automatic watering